## ALLOCATION OF POWER SOCKET MC-ROUND FOR WIENER POWER SUPPLY

Rear View of Power Supply ( SocketMC-Round view)

9U VME64x Crate -Wiener Power Supply Type  LHC Ref : OP04-1080/1180

*) Plug & Play : Software control ligne to check compatiblity between Bin and Power Supply

Empty Spare		Positive Terminal		      Negative Terminal	        Analog Negative Terminal

## OUTPUT VOLTAGE AND CURRENT RATING

9U VME64x Crate –Wiener Power Supply Type : LHC  Ref :	OP04-1080/1180

| Positive Contact | Negative Contact | Output Name | Voltage (V) | Current (A) | Power (W) | No modules |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | 2 | U0 | +5V | 100 | 500 | 1 |
| 10 | 11 | U1 | +12V | 10 | 120 | 1/2 |
| 16 | 17 | U2 | 48V | 36 | 1728 | 3 |
| 7 | 8 | U3 | +3.3V | 100 | 330 | 1 |
|  |  | U4 |  |  |  |  |
| 13 | 14 | U5 | -12V | 10 | 120 | 1/2 |
|  |  | U6 |  |  |  |  |
|  |  | U7 |  |  |  |  |

Contact No.	10, 11, 13….18 :		6mm.	120A max		Total modules :	6

Contact No.	1….9, 12 :			8mm	240A max

### Sense and Signal Connector-SUB  D 37 from Power Supply

| Contact | Description | Contact | Description |
| --- | --- | --- | --- |
|  |  | 19 | TEMP RETURN |
| 37 | TEMP 0 | 18 | TEMP 1 |
| 36 | TEMP 2 | 17 | TEMP 3 |
| 35 | TEMP 4 | 16 | TEMP 5 |
| 34 | TEMP 6 | 15 | TEMP 7 |
| 33 | BIN EEPROM: IIC SDA | 14 | BIN EEPROM: IIC SCL |
| 32 | BIN EEPROM: +5V | 13 | VME LOGIC: SYSRESET |
| 31 | BIN EEPROM: GND | 12 | VME LOGIC: ACFAIL |
| 30 | VME LOGIC GND | 11 | VME LOGIC: SYSFAIL |
| 29 | U0 SENSE – (VME: +5V) | 10 | U0 SENSE + (VME: +5V) |
| 28 | (reserved) | 9 | (reserved) |
| 27 | (reserved) | 8 | (reserved) |
| 26 | U4 SENSE + | 7 | U4 SENSE - |
| 25 | U7 SENSE + | 6 | U7 SENSE - |
| 24 | U2 SENSE – (VME: 48V) | 5 | U2 SENSE + (VME: 48V) |
| 23 | U6 SENSE + | 4 | U6 SENSE - |
| 22 | U1 SENSE – (VME: +12V) | 3 | U1 SENSE + (VME: +12V) |
| 21 | U5 SENSE + (VME: -12V) | 2 | U5 SENSE – (VME: -12V) |
| 20 | U3 SENSE – (VME: +3.3V) | 1 | U3 SENSE + (VME: +3.3V) |

Maximal 8 different floating outputs can be controlled in a single power box (U0... U7)

### Pin Assignment of the Backplane Sense Connector *)

| Pin No | Description | Pin No | Description |
| --- | --- | --- | --- |
| 1 | U3 SENSE + (VME: +3.3V) | 2 | U3 SENSE – (VME: +3.3V) |
| 3 | U5 SENSE – (VME: -12V) | 4 | U5 SENSE + (VME:-12V) |
| 5 | U1 SENSE + (VME: +12V) | 6 | U1 SENSE – (VME: +12V) |
| 7 | U6 SENSE - | 8 | U6 SENSE + |
| 9 | U2 SENSE + (VME: 48V) | 10 | U2 SENSE – (VME: 48V) |
| 11 | U7 SENSE - | 12 | U7 SENSE + |
| 13 | U4 SENSE - | 14 | U4 SENSE + |
| 15 | VX SENSE (reserved) | 16 | VX SENSE (reserved) |
| 17 | VW SENSE (reserved) | 18 | VW SENSE (reserved) |
| 19 | U0 SENSE + (VME: +5V) | 20 | U0 SENSE – (VME: +5V) |
| 21 | VME LOGIC: SYSFAIL | 22 | VME LOGIC GND |
| 23 | VME LOGIC: ACFAIL | 24 | VME LOGIC GND |
| 25 | VME LOGIC: SYSRESET | 26 | VME LOGIC GND |
| 27 | reserved | 28 | reserved |
| 29 | TEMP 7 | 30 | TEMP 6 |
| 31 | TEMP 5 | 32 | TEMP 4 |
| 33 | TEMP 3 | 34 | TEMP 2 |
| 35 | TEMP 1 | 36 | TEMP 0 |
| 37 | TEMP RETURN | 38 | not connected |
| 39 | not connected | 40 | not connected |

*) Male Connector 2x20 pin 2.54mm, for flat cable

# Text boxes

18		         15		        12		      9		6	            3

Spare

6mm socket zone				8mm socket zone	           	            Plug & Play*

17	    	         14		       11		      8		5	            2

48V	       -12V	   +12V		+3.3V	          Spare	        +5V

16	          13		       10		      7		4	            1