2001/06/20

P. Gällnö/CERN/PH/ATE

ROD-BUSY MODULE REGISTER OFFSETS

| Addr. offset | Register | R/W | Access | Remarks | FIFO's + FIFO SEQUENSER |
| --- | --- | --- | --- | --- | --- |
| EE 1110-1110 | FIFEF | R | W 16 | FIFO empty flags |  |
| EC 1110-1100 | FIFFF | R | W 16 | FIFO full flags |  |
| EA 1110-1010 | SEQREG | R/W | W 16 | Sequencer transfer interval register |  |
| E8 1110-1000 | FIFRCR | R/W | W 16 | FIFO read control register |  |
| E6 1110-0110 | FIFWCR | R/W | W 2 | Counter and FIFO write control register |  |
| E4 1110-0100 | FIFWEN | W | W - | Transfer all counters to FIFO's |  |
| E2 1110-0010 | FIFRST | W | W - | Reset all FIFO's |  |
| E0 1110-0000 | CNTRST | W | W - | Reset all counters |  |
| DE 1101-1110 | FIFO-READ-15 | R | W 16 | Busy duration FIFO 15 |  |
| DC 1101-1100 | FIFO-READ-14 | R | W 16 | Busy duration FIFO 14 |  |
| DA 1101-1010 | FIFO-READ-13 | R | W 16 | Busy duration FIFO 13 |  |
| D8 1101-1000 | FIFO-READ-12 | R | W 16 | Busy duration FIFO 12 |  |
| D6 1101-0110 | FIFO-READ-11 | R | W 16 | Busy duration FIFO 11 |  |
| D4 1101-0100 | FIFO-READ-10 | R | W 16 | Busy duration FIFO 10 |  |
| D2 1101-0010 | FIFO-READ-9 | R | W 16 | Busy duration FIFO 9 |  |
| D0 1101-0000 | FIFO-READ-8 | R | W 16 | Busy duration FIFO 8 |  |
| CE 1100-1110 | FIFO-READ-7 | R | W 16 | Busy duration FIFO 7 |  |
| CC 1100-1100 | FIFO-READ-6 | R | W 16 | Busy duration FIFO 6 |  |
| CA 1100-1010 | FIFO-READ-5 | R | W 16 | Busy duration FIFO 5 |  |
| C8 1100-1000 | FIFO-READ-4 | R | W 16 | Busy duration FIFO 4 |  |
| C6 1100-0110 | FIFO-READ-3 | R | W 16 | Busy duration FIFO 3 |  |
| C4 1100-0100 | FIFO-READ-2 | R | W 16 | Busy duration FIFO 2 |  |
| C2 1100-0010 | FIFO-READ-1 | R | W 16 | Busy duration FIFO 1 |  |
| C0 1100-0000 | FIFO-READ-0 | R | W 16 | Busy duration FIFO 0 |  |
| 9E 1001-1110 |  |  |  |  | I/P REG |
| 9C 1001-1100 |  |  |  |  |  |
| 9A 1001-1010 | BUSYMASK | R/W | W 16 | SET/CLR Busy mask |  |
| 98 1001-1000 | BUSYSTATE | R/W | W 16 | Read i/p busy lines / Write test bits |  |
| 96 1001-0110 | IVALREG | R/W | W 16 | Interval Count Register | SREQ TIMER |
| 94 1001-0100 | LIMREG | R/W | W 16 | Limit Count Register |  |
| 92 1001-0010 | SREQSETCLR | W | W 2 | Service Request Set/Clear Functions |  |
| 90 1001-0000 | SREQCSR | R/W | W 4 | Busy/Service Requester CSR |  |
| 8E 1000-1110 |  |  |  |  |  |
| 8C 1000-1100 |  |  |  |  |  |
| 8A 1000-1010 |  |  |  |  |  |
| 88 1000-1000 |  |  |  |  |  |
| 86 1000-0110 | INTID | R/W | W 16 | VME Interrupter Status/ID register | VME I/F |
| 84 1000-0100 | INTCSR | R/W | W 16 | VME Interrupter CSR |  |
| 82 1000-0010 | SWIRQ | W | W - | VME Interrupt by soft function |  |
| 80 1000-0000 | SWRST | W | W - | Reset module / data-less function |  |
| 00 0000-0000 | Config. EEPROM | R/(W) | W 16 | LSBytes in every Long Word. See specs. |  |

CONFIGURATION - IDENTIFICATION EEPROM MAPPING

| VME Address Offsets |  |  |
| --- | --- | --- |
| MSBYTE |  |  | LSBYTE |  |  |
| 31 24 | 23 16 | 15 8 | 7 0 |  |  |
| 20 | 21 | 22 | 23 |  |  |
| 24 | 25 | 26 | 27 | Manufacturer ID (CERN) | MSBYTE |
| 28 | 29 | 2A | 2B | Manufacturer ID (CERN) |  |
| 2C | 2D | 2E | 2F | Manufacturer ID (CERN) | LSBYTE |
| 30 | 31 | 32 | 33 | Board ID / Serial No. | MSBYTE |
| 34 | 35 | 36 | 37 | Board ID / Serial No. |  |
| 38 | 39 | 3A | 3B | Board ID / Serial No. |  |
| 3C | 3D | 3E | 3F | Board ID / Serial No. |  |
| 40 | 41 | 42 | 43 | Board Revision No. | MSBYTE |
| 44 | 45 | 46 | 47 | Board Revision No. |  |
| 48 | 49 | 4A | 4B | Board Revision No. |  |
| 4C | 4D | 4E | 4F | Board Revision No. | LSBYTE |

The IEEE Manufacturer ID# for CERN is: 080030 (hex)